## Slide 1: Muography with nuclear emulsions in Italy
Valeri Tioukov1, Giovanni De Lellis1, Andrey Aleksandrov1, Lucia Consiglio1, Andrey Sheshukov1, Tatiana Shchedrina1, Massimo Orazi2, Rosario Peluso2, Cristiano Bozza3, Chiara De Sio3, Simona Maria Stellacci3, ChiaraSirignano4, Nicola D’Ambrosio5, Seigo Miyamoto6, Ryuichi Nishiyama6, Hiroyuki Tanaka6, Mikhailo Vladimirov7
1University of Napoli / INFN, Italy, 2INGV - Napoli, Italy, 3University of Salerno / INFN, Italy, 4Universityof Padova / INFN, Italy, 5INFN - LNGS, Italy, 6University of Tokio, Japan, , 7LPI - Moscow

## Slide 2: Outlook
Nuclear emulsion laboratories and experiments in Italy
Recent Muon radiography projects with Italian emulsion laboratories involved
Stromboli exposure 22-Oct-2011 - 24-Mar-2012 for 154 days
Potential and prospective of muography with nuclear emulsion in Italy

## Slide 3: Emulsion projects and laboratories in Italy
Main business is fundamental Particle Physics (neutrino experiments in particular)
1990 – 2002 CHORUS experiment
2002 – now OPERA project
Emulsion scanning laboratories in Italy (OPERA participants)
  Napoli, Salerno, Gran Sasso, Bari, Bologna, Padova
  About 30 scanning systems were constructed in Italy for OPERA scnning
Since 2011 – some laboratories are involved in Muography projects
  Napoli, Salerno, Gran Sasso

## Slide 4: The OPERA detector: 8.9 mln films with the total emulsion sensitive surface of 200000 m2
neutrino
10x10x50 meters
apparatus
ECC “brick”
57 emulsion plates
56 lead plates
10x12x7 cm, 8 kg

## Slide 5
Unzen
Stromboli
Teide summit
Muography emulsion projects with
participation of Italian laboratories
Unzen - data analysis is in the final phase
Stromboli – half statistics, first results
Teide – exposure is completed, scanning is started

## Slide 6: The principle of muon radiography
Telescope
10/15/2013
Valeri Tioukov, IAVCEI 2013
6
Nearly horizontal
atmospheric muons cross the mountain
It’s assumed that the muon flux and spectrum well known and nearly constant
Assumed the precise knowledge about the mountain shape
What we can obtain is the angular map of the average rock density using the muons absorption information
Detector should provide precise angle for each particle passed through
The method is limited to the upper part of the mountain above the detector
Low muons rate do not allow to have short exposure – months is a typical time scale
1 km of the rock thickness is an approximate upper limit for 1-few m2 detectors with few months exposure
Emulsion is a good candidate!

## Slide 7: Motivations for the Stromboli exposure
Stromboli is one of the most known and most active volcanoes in the world
Great amount of monitoring equipment is installed on the volcano slopes, but the exact internal structure of the region below craters is not well understood yet
There is a possibility that the explosion source mechanism is representative of two cracks dipping ∼60◦ that are located approximately 220-260 m, beneath the active craters, probably representing parts of an echelon system of fissures
muon radiography can be an independent technique for investigating the internal structure of the cone and revealing the location and extent of the conduits that feed the continuous explosions
Region under “Sciara del Fuoco” is the one of our interest
Motivations for muon radiography of active volcanoes,
G. Macedonio and M. Martini, Earth Planets Space, 61, 1–5, 2009

## Slide 9: Good place for the detector installation was individuated in May 2011 (the only relatively flat at this altitude)

## Slide 10
View from the detector position (640m)
Craters region (750 m)
Sciara del fuoco

## Slide 11: Above 500 m part of the island
Detector
Craters region

## Slide 12: Example of the elevation profile
1.5 km
640 m
Tan =0.24
Stromboli has not so sharp cone - only a part of edifice can be
monitored with a middle-size muon telescope

## Slide 13
Metal plates
of 5mm (inox)
Envelopes with emulsions
glued to the central
inox plate
Aluminum Frame
Elastic (rubber) layers
One module with 10 emulsion “cells”
Each cell has 2 emulsions doublets attached
to both sides of the central metal plate.
Front view of the central plate (26 x 80 cm)
The total weight of one module is of 26 kg
Total amount of emulsions/module: 40
The active surface covered is of 1200 cm2
The overall weight of 8 modules and the support frame is about 250 kg
“Exploded view”
Scheme of the internal module structure

## Slide 14
Emulsions extraction after 5 months exposure. The envelopes are in a good shape

## Slide 15
GPS
Movement sensor
1B
2B
3B
4B
5B
8B
7B
6B
The overall dimension is about 70 x 350 cm, 250 kg

## Slide 16
After 5 months of data taking we found the detector in a good shape well protected from sun heating and from moisture by rubber foam (armaflex) and by expanded clay

## Slide 17
1
3
2
To keep memory about the module orientation 3 fixed vertices were installed and the distances measured with the laser distanziometer (+-2 mm accuracy)
GPS data were recorded on 2 detector and on 2 vertex points

## Slide 18: The data analysis assume the precise knowledge about the mountain shape
Detector position
Area of interest
Only the part of the island above
500m is displayed here
Precise and up to date
Digital Elevations Map (DEM) Is required

## Slide 19
DEM – Photo comparison
Photographs of the mountain taken from the detector position compared to the shape of the DEM viewed from the same point
Precise images coincidence confirms the precision of the GPS coordinates

## Slide 21
DEM – Data comparison
Dem view
Data tx-ty distribution
Dem-data superimposed
Data absorbed part
em-data absorbed superimposed

## Slide 22
10/15/2013
Valeri Tioukov, IAVCEI 2013
22

## Slide 23
The first exercise of data-MC comparison on the incomplete statistics
We observe some data excess in a crater region in respect to MC, this can be a sign of lower density
It is difficult yet to judge about more fine effects
We plan to perform additional study to refine efficiency and background angular dependency corrections
Data subtracted from MC

## Slide 24: Nuclear emulsions as a detector for muon radiography
Advantages
Perfect intrinsic angular resolution (better then 2 mrad)
Compact and easy to transport
No electricity required
Can be installed in a harsh environment
Modular, can be installed inside narrow locations
Disadvantages
No time information (can be solved in some cases)
Complicated and time-consuming data acquisition – required special scanning systems
accepted temperature range for long-term exposures is below 25 C
Single-use sensitive part
Able to provide new information complimentary to
other methods used for volcanoes survey

## Slide 25: Prospective and potential for emulsion muography in Italy
Currently - a by-product of the technology developed for neutrino physics
The scanning power used in Italy for Unzen-Stromboli-Teide emulsions scanning is equivalent to 2 scanning systems used 30% of time
Resent scanning speed is about 20 cm²/h/layer so minimum time required for the full scanning of Stromboli-like detector (1m² x 8 layers) is of 170 days
In a near future (1-2 years) with OPERA load going down the available scanning power may become about 10-20 SS 100% available for muography - this means factor 30 speedup
Scanning systems HW upgrade is coming (see morning talk) with additional factor of 5 minimum increase of the scanning speed
In a short time scale we can acquire a potential to perform the analysis of 1 m² emulsion telescope in just a few days!
This makes emulsions an attractive option also for a large-scale muon telescopes, multy-points exposure (tomography) and for industrial applications

## Slide 26
La Sciara del Fuoco al tramonto
Thank you for your attention!