## Slide 1: Measurement of the fragmentation of Carbon ions with nuclear emulsions for medical applications
Adele LAURIA
On the behalf of Naples emulsion group
University of Naples “Federico II”, Italy
INFN, Naples

## Slide 2
  Hadrontherapy motivation
  The 12C fragmentation measurement with the Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 3
  Hadrontherapy motivation
  The 12C fragmentation measurement
  The Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 4
For hadrons (compared to X and γ):
  Energy deposited at the end of ionization range
Hadrontherapy motivation
For 12C (compared to protons):
  Reduced lateral and longitudinal diffusion;
  Higher therapeutic effectiveness;
  Tissue thickness tunable by changing the nuclei energy;
  Less energy deposited to healthy neighboring tissues

## Slide 5
http://enlight.web.cern.ch/facilities
Facilities in Europe:
Hadrontherapy

## Slide 6
Patient Statistics (for facilities in operation at the end of 2012):
http://enlight.web.cern.ch

## Slide 7
Nuclear fragments are generated during the interaction inside the tissue
Fragments have higher range and different direction with respect to primary ions
Precise knowledge of fragments is necessary to predict the detailed irradiation of the neighboring tissues and, thereby, optimization of the therapy with higher effectiveness
  Fragmentation of 12C
Simulation: A. Mairani PhD Thesis, 2007, Nuovo Cimento C, 31, 2008
12C (400 MeV/n) on water Bragg-Peak
  What we need to know
Kind of fragments
Which energy?
Which angle?

## Slide 8
  Hadrontherapy motivation
  The 12C fragmentation measurement with the Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 9: Carbon exposure at HIMAC* (NIRS**- Chiba(Japan))
Emulsion Cloud Chamber (ECC)
*Heavy Ion Medical Accelerator
**National Institute of Radiological Sciences

## Slide 10: The structure of the Emulsion Cloud Chamber
ECC structure:
  “OPERA” type: alternate passive and sensitive material
  High resolution tracking device: nuclear emulsion (300 µm thick)
  Passive material: lexan plates 1 mm thick
  73 consecutive “cells”: 219 alternate nuclear and lexan layers
Lexan: =1.15 g/cm3 and electron density=3.6∙1023/cm3 (water: 3.3∙1023/cm3)
12C
300 μm
EMULSION LAYER
1000 μm
LEXAN LAYER
Elementary
cells

## Slide 11: The cell structure of the Emulsion Cloud Chamber
LEXAN
LEXAN
LEXAN
12C
1 mm
300 μm
Emulsion were differently treated after the exposure and before the chemical treatment according to their position in the elementary cell (0, 1, 2)
R0:
    Not refreshed
    Developed soon after the exposure
    Sensitive to m.i.p.
R1:
    3 day refreshing at 98% relative humidity at 30°C
    Insensitive to m.i.p.
    Sensitive to protons
R2:
    3 day refreshing at 98% relative humidity at 38°C
    Sensitive to He
R0
R1
R2

## Slide 12: Nuclear emulsion
Charged particle detector
First kind of detector for ionizing radiation
AgBr crystal (0.2 μm) is the elementary detection cell
The particle tracking is registered from the AgBr grains along its path
50 μm
30-40 grains/100 μm per MIP
Microscope image

## Slide 13: OPERA emulsions
Plastic Base (205 microns)
Emulsion Layer (43 microns)
OPERA industrial emulsions from FujiFilm
The AgBr density in the OPERA emulsions is higher in respect to the commercial films
Special R&D for OPERA: the double pouring procedure
150 microns
Emulsions are continuously sensitive detector ALL charged particle: cosmic rays, natural radioactivity etc recorded as a latent images. They can be partially erased by a “refreshing” procedure applied just before the detector assembling.
Before refreshing
>30 tracks/mm^2
After refreshing
~1 tracks/mm^2

## Slide 14: Emulsion scanning system
16
OPERA expertise in scanning
3d track reconstruction
Scanning speed: 20 cm2/h
Spatial resolution: ~0.3 m
• Angular resolution: ~2 mrad
• Detection efficiency of the tracks: ~95%
C
M
O
S
c
a
m
e
r
a
1
2
8
0
×
1
0
2
4
p
i
xe
l
2
5
6
gr
a
y
l
e
v
e
l
s
376 f
r
ames
/s
ec
(Mikr
o
tr
o
n MC1310)
X
Y
s
t
a
ge
(
M
i
c
o
s
)
0.1 µm no
minal
precisio
n
Em
u
lsi
on
Pla
t
e
Z
s
t
a
ge
(
M
i
c
o
s
)
0.05 µm no
minal
precisio
n
Illumination system, objective (oil 50× NA0.85) and optical tube (Nikon)

## Slide 15
16 images taken through 44-micron emulsion layer
Principle of scanning emulsion

## Slide 16
Automatic scanning system
Micro-track reconstruction in one emulsion layer by combining clusters belonging to images at different levels.
Micro-tacks are connected across the plastic base to form a base-tracks.

## Slide 17: Combining the information on consecutive films to get rid of the saturation effect R0 vs R1 and R1 vs R2 scatter plot
H
He
Results
Journal of Instrumentation 2 (2007) P06004

## Slide 18
Charge identification
Z = 2
Z = 3
Z = 4
2 cm thick chamber
4 cm thick chamber
6 cm thick chamber
Z = 4
Z = 3
Z = 2
Z = 5
Z = 6
8 cm thick chamber

## Slide 19: Charge separation
Journal of Instrumentation 2 (2007) P06004

## Slide 20: Scattering angle of emitted particles
Hydrogen
Helium
Lithium

## Slide 21: Cross-section measurement
A volume of about 24 cm3 analyzed
Average energy of the Carbon beam: 315 MeV/n
Counting the events with Lithium (z = 3), Beryllium (z = 2) and Boron (z = 1) as the heaviest particle in the final state
Black points: Phys.Rev.C75 (2007) 054606

## Slide 22: 8Be production Cross Section
8Be  He + He (10-16 s)
Q value 90 keV  small opening angle
Opening angle between pairs of reconstructed Helium tracks
One event
C
p
p
He
He
Peak at 20≈mrad

## Slide 23
  Hadrontherapy motivation
  The 12C fragmentation measurement with the Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 24
  FIRST experiment
FIRST: Fragmentation of Ions Relevants for Space and Therapy
Aim:
  Production yelds of Z=0, 1, 2 ,3 ,4 ,5 fragments
  Measurement of cross section wrt angle and energy, with large angular acceptance
A collaboration among:
  INFN: Cagliari, LNF, LNS, Milano, Napoli, Roma3,Torino;
  DSM/IRFU/SPhN CEA Saclay, IN2P3 Caen, Strasbourg, Lyon;
  GSI:
      Therapeutical beam of 12C @ 200-400 MeV/n available
      Existing setup designed for higher E and Z fragments: Dipole magnet, Large Volume TPC, TOF Wall, low angle Neutron detector.
  ESA, CERN

## Slide 25
What do we expect from MC (FLUKA)?
The Z>2 produced fragments approximately have the same velocity of the 12C beam projectiles and are collimated in the forward direction
The protons are the most abundant fragments with a wide angular distribution and a kinetic energy spectrum up to 1 Gev/n
The Z=2 fragment are emitted within 20°of angular aperture
Kinetic energy (MeV/nucl)
Emission angle (deg)

## Slide 26
  FIRST set up
The measurements were performed at the GSI facilities, where a therapeutical beam of 12C @ 200-400 MeV/n is available
LAND
TIME OF FLY
WALL
VETO COUNTER
Identifies particles coming from primary beam
Fragments
Incident
Beam
Target
6°
KENTROS
Interaction region:
Start counter
Beam monitor
Vertex detector
Proton tagger
ALADIN
Bending magnet
(<6°)
MUSIC
Energy particles
Slope particles

## Slide 27
  Hadrontherapy motivation
  The 12C fragmentation measurement with the Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 28
“FIRST experiment: Fragmentation of Ions Relevant for Space and Therapy”
Journal of Physics: Conference Series 420 (2013) 012061 doi:10.1088/1742-6596/420/1/012061
The FIRST set-up
ECC
12.5cm
10.2cm
ECC
ECC1
ECC2

## Slide 29: Beam exposure of ECC
12C beam with 400 MeV/n
Carbon target (8 mm thick)
Two ECC were collocated inside the detector FIRST
Dedicated study on large angle track detection
2°≤ α2 ≤ 38°
ECC2
ECC1
beam
a ≈ 16.5 cm
b ≈ 0.5 cm
α2
38°≤ α1 ≤ 57°
α1

## Slide 30: ECC strucutre
ECC structure:
Not homogeneous structure
6 consecutive emulsion films
56 nuclear emulsion layers (300 m) interleaved with 56 lead plates (1 mm)
300 m nuclear emulsion
6 consecutive emulsions
1 mm lead layer
ECC
12.5cm
10.2cm
film 1
film 2
film 56
film 57
film 62

## Slide 31
  Hadrontherapy motivation
  The 12C fragmentation measurement
  The Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 32
20 emulsions were scanned (6 consecutive emulsions and 14 emulsions interleaved with lead)
Data were scanned and processed up to tg q ≤ 2
ECC 2: Tracks angular distribution
Signal and cosmic rays
Signal cut:
-0.9 ≤ tg Θx ≤ -0.1
-0.3 ≤ tg Θy ≤ 0.28)
Signal is effectively measured at:
3°≤q≤ 40° (for ECC2)
40°≤q≤ 60° (for ECC1)
as it was expected from the exposition geometry

## Slide 33
Tracks selected:
-0.9 ≤ tg Θx ≤ -0.1
-0.3 ≤ tg Θy ≤ 0.28
number of segments ≥ 2
Cosmic rays
Signal
preliminary results
Signal and cosmic ray
range distribution

## Slide 34: Efficiency vs tracks slope
Cosmic rays
Signal
CR/(S+CR)=24.4%
Reconstruction efficiency
Angular distribution of only signal
corrected by efficiency
preliminary results

## Slide 35: Kinematical measurements 1. Momentum measurement by multiple coulomb scattering (MCS)
p (MeV/c) =
13.6
  (mrad)
X0
x
“Momentum measurement by the angular method in the Emulsion Cloud Chamber”,
Nuclear Instruments and Methods in Physics Research A 512 (2003) 539–545
From the slope measurements along the particle track of the same particle obtained from the ECC it is possible to calculate the particle impulse in the range: 200 MeV/c ÷ 2 GeV/c
The algorithm was used for OPERA experiment and is based on:

## Slide 36
11 % of the total tracks of the sample
preliminary results
Tracks behind the first 6 emulsions
Tracks with at least 3 segments passing through
Kinematical measurements 1.Momentum measurement by MCS

## Slide 37
82 % of the total tracks of the sample
preliminary results
Tracks for which it is not possible the measurement by the MCS method
Tracks stopped in the first 6 emulsions
Tracks not stopped inside the considered volume (20 layers)
Kinematical measurements 2. Momentum measurement by range

## Slide 38
  Hadrontherapy motivation
  The 12C fragmentation measurement with the Emulsion Cloud Chamber (ECC) detector
  The FIRST detector
  Measurements at GSI in the FIRST set-up
  Preliminary results
  Conclusion
Outline

## Slide 39: Conclusions
Emulsion Cloud Chamber technique used to study the fragmentation of Carbon ions
  Homogeneous ECC used as target and detector
  Not Homogeneous ECC used as detector
From these studies:
Discrimination of produced fragments in Z
Charge-changing cross-section measured
Moment measurement with MCS algorithm and range method

## Slide 40: Backup slides

## Slide 41
Interaction length of secondary ions

## Slide 44
0.1≤ tg Θx ≤ 0.9
-0.3 ≤ tg Θy ≤ 0.28)
-0.9≤ tg Θx ≤ -0.1
-0.3 ≤ tg Θy ≤ 0.28
Signal
Cosmic rays
Reconstruction efficiency
Tracks selected:
angle selection
number of segments ≥ 2
Number of plates ≥ 6

## Slide 45: Data (images) processing and motion control flow in the ESS
280×365μm2
Tomographic sequences Z axis moving, 2D images spanning emulsion thickness
Move XYZ to next view
Process/save data
Next field of view, Z at top, new cycle
DAQ cycle (185 ms)
Camera
2D Images (peak 452 MB/s, avg. 97 MB/s)
Image Processor board (Matrox Odyssey)
Binarized 2D Images
Host PC (Dual Pentium Workstation) Running WinXP
3D microtracks
XYZ Motion Commands
Motion Controller (National Instruments FlexMotion)
Motors (VEXTA Nanostep)
Power
Functional blocks

## Slide 46
Films transported from Gran Sasso to CERN
Brick assembled at CERN
Cosmic-ray integrated during the transportation of the brick from CERN to GSI and from GSI to Gran Sasso
Brick disassembled and film developed at Gran Sasso
Cosmic-ray angular distribution
Cosmic-rays taken with the films inside the
brick in the same geometrical configuration
as for the beam at GSI, with the brick rotated
by 90 degrees to minimize the flux